Thursday, February 20, 1992

How To Build NetCDF With Macintosh MPW C.

Dr. Charles R. Denham
Zydeco Scientific Software
45 Hollett Street
North Scituate, MA 02066
(617) 545-8233 (Scituate)
(508) 457-2265 (USGS, Woods Hole)

Introduction

Building NetCDF under Macintosh MPW is fairly straightforward.  I naively
compiled each original routine, then adjusted the source codes whenever the
compiler complained.  The main concerns were several multiple casts to (void),
and the prototyping of variable-argument lists.  I also played with the
compiler directives for _VMS_ and _MACOS_ a bit, until things worked.

I used the MPW "Create BuildCommands..." menu to create a makefile that
gathers the source files for each program or library, and then made additions.
The makefiles were not as comprehensive as those supplied with the NetCDF
sources, but they got the job done.

Here are a few details for NetCDF pre-2.0, but it looks like they
still hold for version 2.02.  

Stamp Out Double Voids

    Declarations of (void) often become interpreted as (void) (void), due
to macros.  The C standard makes it illegal to cast a (void).  Eliminate
any (void) cast that the compiler objects to.  Here is an example from
alloc.h:

    # define m_free(ptr)            free(ptr)        /*    Correct.    */
    
    # define m_free(ptr)    (void)  free(ptr)        /*    Not allowed. */
    
Standard C Flag

    Define the __STDC__ flag, since MPW C does not do it automatically.
Then, in every file that uses variable argument lists, do this:

    # if defined __STDC__
    # include <stdarg.h>
    # else
    # include <varargs.h>
    # endif

Variable Argument List Prototypes

    Convert variable argument lists to standard C by performing in-line
prototyping.  Here is an example from derror.c, part of ncgen.

    # if defined __STDC__
        Void
        derror(char * fmt, ...)
    # else
        Void
        derror(fmt, va_list)
        char *fmt;
        va_dcl
    # endif
    
Compilation Flags

    Set the -d VMS and -d __STDC__ options.

NCDUMP

    Works beautifully.

NCGEN

    I never got it to work.  It chokes part-way through the NetCDF test file.

NCTOOLS

    I build a stand-alone tool for each function in the NetCDF protocol.  The
command-line arguments are arranged as much like the protocol as possible.
One embellishment is that I allowed items to be referenced by name, as well
as by id.  Several versions of ncvarput and ncvarget allow us to be selective
about the source or destination data files outside NetCDF.  We currently
handle flat ascii, flat binary, and Matlab binary Mat-files.

MCTOOLS

    I also built Matlab analogs of the NCTOOLS, so that we could interact
with NetCDF files from within Matlab.  On the Macintosh, which lacks true
multi-tasking, the use of these tools is very tricky, so we often just use
the NCTOOLS directly by running under MultiFinder and switching to MPW when
we need data.

    I built a little server that runs in the background under MPW to handle
NetCDF requests from Macintosh Matlab.  It is slow and not completely
automatic, so often I switch to MPW manually under MultiFinder and use the
NCTOOLS directly.

    An alternative approach would be to write a NetCDF desk accessory, or
to develop a real server under System 7.0.

    Some WHOI colleagues have build Mex-file versions of the protocol, for
big gains in speed.